## File Descriptors and System Calls
### 1. File Descriptors
- Definition: A file descriptor (FD) is an integer that identifies an open I/O stream like files, network connections, terminals, or pipes.
- File Descriptor Table: It is an array of kernel objects where file descriptors are indexes.
- Components:
  - File Reference: Path of the file, e.g., /home/example.txt.
  - File Position: Offset in the file indicating the current position.
- Types of Files:
  - Seekable: Position can be explicitly changed (e.g., disk files).
  - Non-Seekable: Position cannot be changed (e.g., pipes, terminals).

### 2. System Calls
- Definition: A request made by a user program to the OS for performing privileged operations.
- Steps:
  - Save CPU state → Switch to kernel mode → Perform the operation → Return result to user space.
- Why Expensive?: It involves context switching, state saving, and kernel intervention.

### 3. System Calls vs. Function Calls
Aspect	Function Call	System Call
Domain	User-level only	Kernel-level intervention
Security	Trusted environment	OS has super-privileges
Speed	Faster	Slower due to context switching

- Example:
  - Function Call: fopen()
  - System Call: open()

### 4. Sequence of a System Call
- Steps:
  - Use a software interrupt to switch to kernel mode.
  - System call number (e.g., read()) is placed in EAX register.
  - Kernel function performs the requested action.
  - CPU restores state and returns control to the user program.

### 5. Important System Calls
- File Management: open(), read(), write(), close(), lseek().
- Process Management: fork(), exec(), getpid().
- Advanced Calls: pipe(), dup(), unlink().

### 6. Standard Input, Output, and Error
- FD 0: Standard Input (stdin)
- FD 1: Standard Output (stdout)
- FD 2: Standard Error (stderr)

### 7. Example Code
Open and Read a File:
c

#include <fcntl.h>
#include <errno.h>
#include <unistd.h>
#include <stdio.h>

int main() {
    int fd = open("file.txt", O_RDONLY);
    if (fd < 0) { perror("Error"); return 1; }

    char buffer[20];
    int sz = read(fd, buffer, 10);
    buffer[sz] = '\0'; // Null-terminate the string
    printf("Read: %s\n", buffer);

    close(fd);
    return 0;
}

## Linux Device Drivers
### 1. Device Drivers
- Definition: Software that allows the OS to communicate with hardware devices.
- Main Role: Translates user-level commands into hardware-specific operations.

### 2. Why Use Device Drivers?
- They act as interfaces between:
  - Applications ↔ Operating System ↔ Hardware.

### 3. Classes of Device Drivers
1. Character Devices:
  1. Handle data one byte at a time.
  2. Examples: /dev/tty (terminal), /dev/console.
2. Block Devices:
  1. Handle data in blocks (512 bytes or larger).
  2. Examples: Hard disks, USB drives.
3. Network Devices:
  1. Transfer packets of data.
  2. Example: Ethernet (eth0).

### 4. Loading Device Drivers
- Kernel Modules:
  - Drivers can be loaded dynamically into the kernel without recompiling.
  - Commands:
    - Load Module: insmod <module>
    - Remove Module: rmmod <module>

### 5. Writing a Simple Device Driver
Hello World Driver Example:
c

#include <linux/module.h>
#include <linux/kernel.h>
#include <linux/init.h>

MODULE_LICENSE("GPL");

static int __init hello_init(void) {
    printk(KERN_INFO "Hello, world\n");
    return 0;
}

static void __exit hello_exit(void) {
    printk(KERN_INFO "Goodbye, world\n");
}

module_init(hello_init);
module_exit(hello_exit);
- Commands:
  - Compile with make.
  - Load module: insmod hello.ko.
  - Remove module: rmmod hello.

### 6. Security Concerns
- Buffer Overflow: Ensure memory is not overwritten.
- Privilege Restriction: Only root users can load modules.
- Uninitialized Memory: Zero out kernel memory before exposing it to user space.

### 7. Device Management
- Inserting Driver:
  - Previously: Kernel had to be recompiled.
  - Now: Use runtime modules (simpler and efficient).

### 8. Important System Calls
- File System:
  - open(), read(), write(), close().
- Device Control:
  - Uses ioctl system calls for custom device management.